## Slide 1
MACRO-Korea: open technical questions
Provincial power-sector model · 17 provinces · 8,760 chronological hours · 2021–2050 myopic
Six questions where the answer depends on how MacroEnergy itself works.
Results shown are from 13 October and predate three staged base-year fixes.
Hanwoong Kim · Net Zero Korea

## Slide 2
STATUS
Where the model is
Structure
Complete. 7 periods, 8,760 h, linear-relaxed UC, myopic, Gurobi barrier.
Solve
Ref 2.5 h · NDC 4.6 h on 24 cores / 192 GB. ~13.6M rows.
Transmission
99.1 GW network from NREL ITLs, calibrated to the KPX metro limit. Expands.
Base year
NOT calibrated. Coal 300 TWh vs 198 observed; gas 58 vs 167.
Staged fixes
Coal availability 0.65 · nuclear 0.85→0.78 · 2021 gas retirement blocked.
Notes: This is the model descriptions.

## Slide 3
CONTEXT
The results you are about to see predate the base-year fix
Flagged so the known gap is not re-diagnosed. Fixes are staged, not yet run.

## Slide 4
QUESTION 1 · HIGHEST PRIORITY
MaxNewCapacityConstraint is per-asset, so we cannot cap a national build rate
Is a grouped / system-wide MaxNewCapacityConstraint available upstream? If not, is user_additions the right place for a custom one?

## Slide 5
QUESTION 2
MinFlowConstraint on all five thermal technologies ran us out of memory
Rows, MinFlow on coal + gas CCGT only
13.60 M
Rows, MinFlow on all five
14.05 M
Added by three technologies
≈ 450,000 rows
Outcome at 128 GB
killed — two jobs
Current state
off for nuclear, coal CCS, gas CCS; mem raised to 192 GB
min_flow_fraction values are still in the CSVs for those three technologies but the constraint is not declared.
Is that row growth expected? Is there a cheaper MinFlow formulation under relaxed UC — and are the undeclared min_flow_fraction values truly inert?

## Slide 6
QUESTION 3
Nuclear is completely rigid, and the carbon price absorbs the consequence
What is the idiomatic way to represent near-baseload nuclear in MACRO? Drop MustRun for a low min_flow_fraction instead?

## Slide 7
QUESTION 4
Transmission: signed bidirectional edges, and a transport formulation
Does MACRO offer DC power flow? To charge a per-MWh cost, should each corridor be split into two unidirectional edges?

## Slide 8
QUESTIONS 5 AND 6
Solution algorithm, and staging a sector that does not exist yet
Q5 · Myopic vs perfect foresight
NDC builds 14.9 GW of nuclear in the single
2025–2030 period, with no build-rate limit.
Myopic now: 17–19 min per period,
2.5 h (Ref) and 4.6 h (NDC) end to end.
Is perfect foresight tractable at 8,760 hours
by 7 periods? What does it cost?
Q6 · Heat demand with no supply
17 Steam nodes carry demand but no asset
produces Steam.
76,212 GWh is non-served every period in
every scenario, identically.
Best practice for staging a sector: drop the
nodes, or keep them at zero penalty?
Heat is the next sector, due November 2026.
Q6 matters now: it determines how we wire the heat sector in next month.

## Slide 9
SHORTER ITEMS
Three things to confirm
HydroRes duration is 475 hours
1,471.8 GWh of storage against 3.1 GW of turbine, fixed in every period. Generates only 0.6 TWh.
Looks inherited from the MacroEnergy example data — can you confirm the provenance?
Battery picks 5.6–5.7 h duration
Given a 2–10 h range, the model settles here in both cases. Plausible, but worth a sanity check.
Solver settings
Barrier, Method=2, Crossover=0, BarConvTol=1e-3, Threads=22, BarHomogeneous=1,
over 8,760 hours in a single subperiod. Any advice?

## Slide 10
SUMMARY
What we are asking for
1
Grouped MaxNewCapacityConstraint
unblocks every build-rate limit we need
2
A cheaper MinFlow formulation
or confirmation that 450k rows is simply the cost
3
The right construct for near-baseload nuclear
drives the carbon price and the curtailment
4
Transmission: DC flow, or split edges
we are using loop-flow ITLs in a transport model
5
Is perfect foresight tractable here
affects how we read the nuclear build path
6
How to stage an unbuilt sector
needed before heat, next month
Priority: 1 and 3. They decide whether the solar and carbon-price results are defensible.